## Slide 1: Emerging Climate Threats to Utility Infrastructure
NGA Spring Operations Conference
April 2025

## Slide 2: THIRA Overview – Purpose:
Due increasing frequency of storms, restoration costs and climate driven threats, Eversource has identified the need for a holistic approach to prioritizing efforts related to both Response and Recovery efforts, as well as Prevention and Mitigation efforts related to Natural Hazards.
Establish a formal THIRA (Threat and Hazard Identification and Risk Assessment) process for Natural Hazards (focused on Today thru 5-Years):
  What hazards are likely to impact the northeast region of the United States (Probability)?
  What impacts would those hazards have on our infrastructure (Vulnerability)?
  What effect would those hazards have on our customers / business (Consequences)?
Prioritize efforts related to update of Eversource All Hazard Emergency response Plan (AHERP) and associated hazards / risk specific documentation.
Prioritize efforts related to investments for Prevention/Mitigation efforts as well as Response/Recovery efforts.
* Eversource Natural Hazards include 18 FEMA identified Natural Hazards (https://hazards.fema.gov/nri/natural-hazards) plus Space Weather (https://www.swpc.noaa.gov/)

## Slide 3
All Hazards Emergency Response Plan
Business Unit Emergency Response Plan
Natural Hazard Threat Assessment
Asset Value / Coverage
Vulnerability Assessment
Incident Response
Analyze Long-Term Capital Program
Analyze how resiliency / mitigation options affect asset
Prioritized Risk Assessment
Hazard Specific Annex
System Reliability / System Growth
Long-Term Climate Change
Hazard Mitigation Options
Liability Analysis
Cost / Benefit
Analysis
Response Strategy
Response Process
Operations / Engineering
Enterprise Risk Management
Emergency Preparedness
Benefits:
Identify / prioritize threats and hazards against infrastructure
Wholistic approach that synchronizes all aspects of the business:
  Asset liability underwriting
  Long-Term Capital Program
  Gas / Electric Interdependency
Comprehensive Risk / Incident Management Program

## Slide 4: Emergency Preparedness – THIRA Assessment
Step 1: Identification of Threats and Hazards of Concern
Assess the eighteen (18) natural hazards as outlined in the National Risk Index (NRI) which included the following:
Avalanche Coastal Flooding Cold Wave
Drought Earthquake Hail
Heat Wave Hurricane Ice Storm
Landslide Lightning Riverine Flooding
Strong Wind Tornado Tsunami
Volcanic Activity Wildfire Winter Weather
In addition to the NRI’s 18 Natural Hazards, this analysis also included Space Weather (i.e. Solar Flares) for a total of nineteen (19) hazards for assessment
Step 2: Utility Infrastructure Vulnerability Assessment
Assess infrastructure vulnerability by evaluating severity and assigning a numerical value using the existing Business Unit Emergency Response Plan Event Level Matrix.
Step 3: Hazard Impact Assessment
Evaluate the expected consequences of an incident, assuming the hazard occurred at different severity levels. This assessment will utilize the existing Business Unit ERP Event Levels (ERP Level 1-5)
The final hazard risk score, derived from this process, produced a prioritized list of hazards requiring the most urgent attention. Once the risks are ranked, capability priorities will be established to address gaps in preparedness and response.

## Slide 5: Emergency Preparedness – Hazard Specific Planning
Threat & Hazard Identification
(Natural, Man-Made, Technology)
Risk Assessment
(Threat, Vulnerability & Consequence)
Risk Controls
(Engineering, Mitigation, Prediction, Preparedness, Response)
Risk Control Evaluation
(Internal & External Audit, KPI's, Training & Exercise Program)
Risk Assessment Validation
(Eversource Risk Committee)
Risk Control Validation
(Eversource Risk Committee)

## Slide 6
  The IMT activates and investigations begin when the severity of the quakes reach 3.0 magnitude within the service territory.
  Tools from the United States Geological Survey (USGS) are used to understand the impact of the earthquake
      USGS Earthquake Notification
      USGS ShakeMap
      USGS “Did You Feel It?” Map
Emergency Preparedness – Earthquake Annex
Notification Process

## Slide 7
The Eversource GIS Department will provide mapping to analyze the location and impact of the earthquake in relation to gas infrastructure and facilities.
  This will assess what infrastructure may have been impacted and start investigations to that designated area.
Emergency Preparedness – Earthquake Annex
MMI 3
Original MMI 3
Damage Assessment Process

## Slide 8: Response Considerations
Mobilization
  Develop safety messaging, including information about if personnel should respond to a location or shelter in place. (Safety Officer)
  Develop earthquake-specific internal communications to keep employees informed of the earthquake effects and the implementation of this Appendix plan. (Communications Officer)
  Use Graphic Information System (GIS) mapping to focus on older material types (such as cast iron) pipes in the sections of the distribution system closest to the earthquake’s epicenter. (Planning Branch Director – Engineering)
  Identify potential system impacts based on the scope of the mapped impacted areas and publish a predicted impact assessment to include potentially impacted customers. (Planning Section Chief)
  Implement engineering survey of LNG/LPG Facilities
  Coordinate with the Operations Section Chief to determine whether the mapped impacted area(s) should be isolated and provide that decision to the IC for approval. (Planning Section Chief)
  Notify dispatchers of the earthquake and track any customer calls in the impacted area with an emphasis on gas odor or no gas calls in a clustered area, or anything indicative of a main break. (Gas Dispatch Branch Director)
Notes: Pick 5 or 6 of the phase across the board

## Slide 9: Response Considerations
Sustained Actions
  Notify and update communities and key stakeholders of any planned isolations being implemented to protect the system after notification of an earthquake event. (Liaison Officer)
  Coordinate with the Gas Operations Section Chief to prioritize repair operations and to determine if any additional isolation measures should be taken. (Planning Section Chief)
  Identify any Critical Facilities affected by the earthquake and coordinate with Engineering to develop potential temporary restoration solutions. (Planning Section Chief)
  Work closely with the Gas Operations Branch Director to determine mapping and list of customers affected by the earthquake. (Planning Branch Director-Tactical)
  Ensure that mark outs are still in place or are replaced in a timely manner; notify contractors, highway departments, and others involved in post-earthquake restoration activities of the presence of pipelines and the risks posed by reduced cover. (Technical Services Branch Director)
  Contract for LNG Tank Assessment

## Slide 10: Response Considerations
Demobilization
  Occurs after all inspections have been made to all the potentially effected infrastructure.
  If damages were found, repairs have been made on the system and there are no area of concerns still pending.
  A duration of time should be monitored within the ICC from the time the first earthquake occurred to the deactivation of the ERP to ensure no aftershock wave activity is detected.

## Slide 11: Jennings Creek Wildfire
Geoff Greene – Senior Specialist, O&R Emergency Preparedness

## Slide 12: Jennings Creek Wildfire
Nov 8
O&R first aware of Jennings Creek Wildfire activity
Nov 22
100% containment declared
Nov 23
100% controlled
427 fire companies & 1,300 firefighters assisted
Nov 9
Nov 13
Nov 16
O&R began response activities
24-hour support continued through November 19th
Orange County declared State of Emergency
Voluntary evacuations conducted

## Slide 13: Jennings Creek Wildfire
Nov 8
O&R first aware of Jennings Creek Wildfire activity
Nov 22
100% containment declared
Nov 23
100% controlled
427 fire companies & 1,300 firefighters assisted
Nov 9
Nov 13
Nov 16
O&R began response activities
24-hour support continued through November 19th
Orange County declared State of Emergency
Voluntary evacuations conducted

## Slide 14: Jennings Creek Wildfire Electric Distribution
Total impacted area
  5,307 acres around Sterling Forest State Park
Customer outages to facilitate firefighting activities
  East side of Greenwood Lake
    New York – 793 customers
    New Jersey – 192 customers
Total impacted area
  5,307 acres around Sterling Forest State Park
Customer outages to facilitate firefighting activities
  East side of Greenwood Lake
    New York – 793 customers
    New Jersey – 192 customers

## Slide 15: Jennings Creek Wildfire Electric Transmission Operations
Transmission Lines join on common tower
  Potential loss of several Substations
  ~15k customer impact with minimal recovery via distribution ties
Coordinated efforts with Fire Rangers to identify alternate fire break lines
Winds ultimately shifted from N/NW to S/SE
Fire Break

## Slide 16: Jennings Creek Wildfire Support Provided
Operations/Emergency Preparedness
    Staffed NY/NJ Command Posts
Distribution Control Center
    Coordinated customer notifications
Line Crews
    Conducted line patrols
    Emergency switching
Vegetation Management
    Cleared ~350 trees
    Cleared brush and other fuels

## Slide 17: Jennings Creek Wildfire Gas Operations
Initial contingency isolation plans
Wah Ta Wah Park was greatest risk of fire impact
  52 customers
November 16th
  Wildfire within 1,000 feet
  Shutdown trigger was mandatory evacuations
November 18th
  Fire lines held
  Voluntary evacuation lifted

## Slide 18: What a Difference a Week Makes

## Slide 19: Next Steps
Wildfire Response Plan
Training and annual exercise
Customer communications plan
Design considerations
Lessons learned
Drone applications

## Slide 22: Q&A
Points of Contact
  Josh White, Director - Gas Emergency Preparedness & Business Continuity
  Joshua.White@eversource.com
  - Geoff Greene - Sr. Specialist, Emergency Preparedness
  Greeneg@oru.com