## Slide 1
Class Location
Notes: It is required that all pipelines have a Maximum Allowable Operating Pressure (MAOP) determined. Once this value is established, the only way that the MAOP can be exceeded is in the case of equipment failure or in the case of the startup and shutdown of a pipeline which is addressed in §192.605. The latter, is normally associated with a pipeline at a compressor station.
The critical part of establishing MAOP is maintaining the records for every segment of pipe, fitting or component put in a system. Provided that the records are in place, segment MAOP’s are established as are also system MAOP’s.
MAOP determination is one of the most difficult sections of Part 192 to understand. This is because we are directed to so many sections of Part 192. Since this is the case, we will be looking at a steel pipeline and then a plastic pipeline.

## Slide 2: Class Location Definition §192.5
The class location unit is an onshore area that extends 220 yards on either side of the centerline of any continuous 1-mile length of pipeline.
The class location is determined by the buildings in the class location unit. For the purposes of this section, each separate dwelling unit in a multiple dwelling building is counted as a separate building intended for human occupancy.
Notes: One other additional subject that we need to discuss while we are in Subpart A is the “Class Location” definition. This is addressed in §192.5.
The “class location unit” is a corridor or rectangle 440 yards wide and 1 mile long with the pipeline in the center. The determination is by counting the houses or buildings intended for human occupancy.
For an apartment complex or condominium structure, each individual apartment is counted as a separate building. For example, if you have an apartment complex with 150 apartments you would have 150 buildings.

## Slide 3: Class Location Unit
A Class 1 = 10 or less buildings intended for human occupancy or an offshore area.
A Class 2 = Greater that 10 but less than 46 buildings intended for human occupancy.
A Class 3 = 46 or more buildings intended for human occupancy; or
Notes: Illustrated above is the house count in the class location unit. As the house count goes up, so does the class location. As the class location increases the design pressure for pipeline is de-rated or decreases.

## Slide 4: Class Location Unit
Class 3 - where the pipeline lies within 100 yards of either a building or a small,
Well-defined Outside Area
  Playground
  Recreation Area
  Outdoor Theater
Occupied by 20 or more persons on at least 5 days a week for 10 weeks in any 12-month period
Notes: This second “Class 3” location regulation was developed based upon some concerns that came out of Texas. The concern was for those areas out in rural communities where there were groups of people gathered close to the pipeline. This amendment or change to the regulation is commonly called the “rural church amendment.” In rural farming communities the churches are built at a crossroads of a highway and then a pipeline is discovered close to the church. For example in the bar ditch across the road.
As an operator, when these areas or structures are discovered along the right-of-way, the use of these areas or structures must be determined.

## Slide 5: Class Location Unit
Class 4 - where buildings with four or more stories aboveground are prevalent.
Notes: The difficulty with “Class 4” determinations is the term “prevalent.” In Webster’s Dictionary, “prevalent” is defined as the “majority of.” The operator needs to make this determination in comparing houses or dwelling units to the number of buildings in the class location unit.

## Slide 6
M.P. 0
M.P. 1
M.P. 2
M.P. 3
46
Class 1
Class Location Determination
M.P. = Mile Post
1 mile
220 yards
9
Notes: The proper way to determine the class locations on a pipeline is by starting at the beginning of the pipeline segment and “sliding” the unit (a 1 mile by 440 yard corridor) down the pipeline looking for the highest concentration of dwellings. This corridor is centered on the pipeline so a person is looking at a distance of 220 yards on either side of the pipeline. It doesn’t matter where the starting point is, the sliding mile determines the highest concentration of dwellings going in either direction. The sliding mile will set the precedence for the class location unit.
In the illustration above, the corridor is started at the beginning of the line. The only buildings that are adjacent to this pipeline are individual homes. The number of houses in the first mile or class location unit is 7. This means this first class location unit is considered to be a Class 1 area.

## Slide 7
M.P. 0
M.P. 1
M.P. 2
M.P. 3
Class 2
46
Class 1
Class 2
Class 1
Continuous Sliding Mile
9
Notes: As the corridor is slid down the pipeline to the next group of houses, the count increases to 14 and the class location unit becomes a Class 2 area. Once a higher class location has been determined, the length of lower class is overridden. Thus a lower class location can be less than a mile long as illustrated above.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 8
Class 2
Class 3
46
Class 1
Class 2
Class 3
Class 1
Continuous Sliding Mile
9
Notes: As you slide down the pipeline, the class locations are adjusted when a higher class location is determined. This third slide of the corridor is to the downstream side of a large group of homes. The house count is 55 in the class location unit, making this area a Class 3. The higher class location starts at the beginning of the corridor and reduces the length of the upstream Class 2 to less than a mile in length.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 9
Class 2
Class 3
46
Class 1
Class 2
Class 3
Class 3
Class 1
Continuous Sliding Mile
9
Notes: As the corridor is slid to catch the next home, 9 homes drop out of the corridor. Because of the big group of homes and the 3 homes at the end of corridor makes the count 49 home, the length is Class 3. As illustrated above, the higher class locations can have an area longer than a mile.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 10
Class 2
Class 3
46
Class 1
Class 2
Class 3
Class 3
Class 2
Class 2
Class 1
Continuous Sliding Mile
9
Notes: Moving on down the pipeline to the next home, houses drop out of the corridor on the upstream side and the house count drops below 46 making a Class 2 area. Because a higher class location has already been determined, the Class 2 does not reduce the length of the Class 3 area.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 11
Class 2
46
Class 1
Class 2
Class 3
Class 3
Class 2
Class 2
Class 3
Class 2
Class 1
Continuous Sliding Mile
9
Notes: As the class location unit is slid down the pipeline, houses drop off the upstream side of the unit increasing the length of the Class 2.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 12
Class 2
46
Class 1
Class 2
Class 3
Class 3
Class 2
Class 2
Class 2
Class 3
Class 2
Class 1
Continuous Sliding Mile
9
Notes: As the class location unit is slid down the pipeline, houses drop off the upstream side of the unit but the count is still high enough for a Class 2 location.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 13
Class 1
Class 2
Class 1
Class 2
Class 3
Class 3
46
Class 2
Class 2
Class 2
Class 1
Class 3
Class 2
Class 1
Continuous Sliding Mile
9
Notes: As the class location unit is slid down to the end of the pipeline, the house count in the class location unit equals 7. This establishes a Class 1 area. Because higher class locations have been established on the upstream side of this last movement of the class location unit, only the very end is considered Class 1. As illustrated above, the higher class location sets the precedence, thus making the higher class location longer than a mile and the Class 2 and Class 1 shorter than a mile.
The overall class location is noted on the top and the individual movement of the corridor on the bottom.

## Slide 14
M.P. 0
M.P. 1
M.P. 2
M.P. 3
46
Class 1
Class Location Determination
9
Notes: Some operators have made the mistake of laying the corridor out mile by mile. Applying the regulation this way can cause the line to be under classified.

## Slide 15
M.P. 0
M.P. 1
M.P. 2
M.P. 3
46
Class 1
Class 3
Class Location Determination
9
Notes: Moving down the pipeline in 1 mile increments or laying the class location unit end-to-end is the incorrect way to determine class locations.

## Slide 16
M.P. 0
M.P. 1
M.P. 2
M.P. 3
46
Class 1
Class 3
Class 1
Class Location Determination
9
Notes: As illustrated above, by using the corridor laid end-to-end, the class location units are just one mile in length. In this application one vital qualifier is left out. That is, “continuous.” To properly apply this regulation, the continuous mile is a sliding mile (§192.5(a)(1)) looking for the highest concentrations of people.

## Slide 17
Class 1
Class 2
46
Class 3
Class 2
Class 1
Continuous Sliding Mile
Class 1
Class 3
Class 1
End-to-End Mile
9
Notes: If you compare the application of the sliding mile versus the end-to-end for the same pipeline, you can see how a pipeline can be under classified by placing a mile end-to-end.

## Slide 18: Clustering
Notes: In §192.5 under paragraph (c), an operator is given the ability to “cluster” or reduce the amount of pipe that is effected by a higher class location.
A different class location of a segment of pipe is effected by several different areas of the regulations. These include design, operations and maintenance.
The regulation states:
The length of Class locations 2, 3, and 4 may be adjusted as follows:
(1) A Class 4 location ends 220 yards (200 meters) from the nearest building with four or more stories above ground.
(2) When a cluster of buildings intended for human occupancy requires a Class 2 or 3 location, the class location ends 220 yards (200 meters) from the nearest building in the cluster.

## Slide 19
46
Class 3 (Established by Sliding Mile)
Clustering
9
Notes: In the example above, 55 homes are at one end of the unit with 3 homes at the other end of the unit. The class location unit is a class 3 established by the sliding mile.
The limits of the class location can be reduced to a length of 220 yards upstream and downstream from a group of buildings.

## Slide 20
46
Class 3 (Established by Sliding Mile)
Clustering
220 yards
220 yards
220 yards
220 yards
9
Class 3
Class 3
Class 1
Class 1
Notes: By clustering, the amount of effected pipe that is subject to Class 3 requirements is reduced.

## Slide 21
44
Class 3 (Established by Sliding Mile)
Incorrect Clustering Application
220 yards
220 yards
220 yards
220 yards
Class 2
Class 1
Class 1
Notes: It is important to understand the correct application of “clustering.” It has been discovered that some operators are “downgrading” a class location or dropping to a lower class locations after the application of clustering. This is an incorrect way to apply clustering.
In the example above, this segment of pipe is in a Class 3 location based upon the sliding mile. After the operator clustered the groups of buildings, they recounted the buildings in the cluster to establish the class location.
Paragraph (c) of 192.5 states:
(c) The length of Class locations 2, 3, and 4 may be adjusted as follows:
(1) A Class 4 location ends 220 yards (200 meters) from the nearest building with four or more stories above ground.
(2) When a cluster of buildings intended for human occupancy requires a Class 2 or 3 location, the class location ends 220 yards (200 meters) from the nearest building in the cluster.
It states the length can be adjusted, not the actual class. The regulation does not allow the operator to downgrade a class location after it has been established by the sliding mile.

## Slide 22
Clustering Limits
220 yards
Perpendicular Method
220 yards
Reduced Class Location Length
Notes: To determine the actual length of a class location based on clustering, OPS has allowed 2 different methods. The inspector will encounter both of them in the field. Even though the distance is will be different, both ways are allowed to be used by an operator as long as they use the same method for the entire length of pipeline.
The perpendicular method is the most commonly used. Illustrated above is a group of homes to be clustered.
For the perpendicular method, the operator would first determine the homes on the furthest point upstream and downstream of the cluster. A perpendicular line is now drawn from the extremity of these homes to the pipeline. Going 220 yards upstream and 220 yards downstream these lines establish the reduced class location length.

## Slide 23
Clustering Limits
220 yards
Arc Method
220 yards
Reduced Class Location Length
Notes: The arc method is the other type of method. Just as illustrated in the previous slide, above is a group of homes to be clustered. For the arc method, the operator would first determine the homes on the furthest point upstream and downstream of the cluster. From the extremity of these homes a line that is 220 yards long is drawn in an arc to the pipeline. At the points where the arc crosses the pipeline is where the beginning and ends points of the class location are established.

## Slide 24
Class 3 – Small Well Defined Area
100 yards
Class 3 Location
School with Playground
100 yards
Notes: The last item that needs to be discussed concerns a small well defined area discovered within 100 yards of a pipeline. If it is occupied by 20 or more person at least 5 days a week, then it is considered a Class 3 location. The questions is, how long is the Class 3 location?
Discussed in the preamble to the final rule that added this paragraph in the code, the limits of the Class 3 is determined by striking a 100 yard arc from the extremities of the building or area. It is important to take in consideration of surrounding areas and not just a building when establishing the length of the Class 3 area. If there is a playground associated with a school, the playground also needs to be included.
In the illustration above, the limits of the Class 3 location are determined by striking a 100 yard arc from the extremities or the further most downstream side and from the further most upstream side. Where the arc strikes the pipeline, these point establish the boundaries of the Class 3 location.